## Slide 1: Alignment NOtes

## Slide 2: Electrical/Computer
XY-Tables Controlled by a computer with parallel 25 pin D-connector interface (Laptops don’t have this connector)
Need a long cable routed outside the cave
Need to install PCI card on the back of one of the nHe-3 computers to operate XY-Tables

## Slide 3
Dimensions of XY Tables:
Large Table:
Length: 50.5 inches
Height(From floor): 49.5 inches
Small Table
Length: 26 inches (Not including end mounts)
Height(From floor): 29.25 inches
XY Tables

## Slide 4: Two Mounts on Large XY Table
Extra Mount?

## Slide 5: Mount for Small XY Table

## Slide 6: Cabling for XY Tables
Power cable for beam monitor (Battery operated)
Signal cable from beam monitor to pre-amp
Power Cable for preamp
Signal cable from pre-amp to DAQ
Power/Signal cable from XY table to Computer

## Slide 7: Placement for small XY table?

## Slide 9: Laser Beam
Melles Griot: Class 3b 633nm CW
Beam emitted at both ends
Outputs 4mWatts at each end
Beam is ~1/8 inch diameter at close range
Safety Requirements apply

## Slide 10
Mount for Laser Beam
Newport Model 39
Two-axis tilt platform
-3.5 to 14 degrees on long axis
-5 to 16 degrees on short axis

## Slide 11: Mount for Laser Beam
Newport model 460P – 90BK
90 degree angle bracket
Newport DS40-XY linear stage
0.55 inches travel in both directions

## Slide 12: Determine Beam Centroid
X1,Y1
X1,Y4
Data points are ordered triples:
Beam Centroid Determined from data from large/small xy-tables:

## Slide 13: Beam Centroid
Need a plan for taking data points
4 Jaw Collimator
Square hole aperture