## Slide 1: Resonant Frequency Spin Rotator For the n3He Experiment
Christopher Hayes
University of Tennessee, Knoxville

## Slide 2: Neutron Scattering on He-3
Goal is Statistical Observation of Parity Violation in the Hadronic Weak Interaction (HWI)
Observable is which represents a correlation between the spin of the incoming neutron and the momentum of the outgoing proton

## Slide 3: Details of the Experiment
Begin with a pulsed source of cold Neutrons (60 Hz)
Neutrons spins are aligned in a super mirror polarizer and the longitudinally polarized
Flip individual pulses of neutron spins
Strike a target filled with He-3 at 1 Atmosphere

## Slide 4: Rotating Neutron Spins
x
z
y
Neutron Beam Direction
Spin Rotator
Helicity = +1
Helicity = -1

## Slide 5: Cosine-Theta Coil
Produce a constant interior B-field by:
1. Wrapping wires longitudinally and parallel to the axis of coil
2. Spacing wires in a cosine winding pattern around the perimeter of the coil.

## Slide 6: Fields of a Cosine Theta Coil
Surface Current Density:
Magnetic analog of electrostatic problem using a charge density glued to the cylinder wall.

## Slide 7: Cosine Theta Coil For n3He Experiment?
Field of a Cosine Theta Coil will not work for the n3He experiment
Spin Rotator is placed next to the target chamber
External B-field interferes with delicate electronics and data acquisition producing uncontrollable false asymmetries
DAQ is Ineffective with an external B-field

## Slide 8: Fields of a Double Cosine Theta
Two Concentric Cosine theta coils
Currents flow in opposite directions

## Slide 9: Pictures of the Double Cosine Theta Coil
Coil has a length of about 16.0 inches
Coil has outer diameter of about 16.5 inches
Inner cylinder constructed from PVC pipe
Outer coils made of plastic

## Slide 10: Pictures from CAD Drawings
360 wires along inner radius
248 wires along outer radius
Coil uses 868 feet of wire

## Slide 11: Inductance of Cosine-Theta Coils
Theory of a double cosine-theta coil allows for an exact calculation of inductance using
CTC:
DCTC:

## Slide 12: Double Cosine-Theta Coil as an RCL Circuit
RFSR
R = 9.11 ohms L = 2.01 mH
Resonance Testing completed
Successful B-field Measurements internal and external to the coil

## Slide 13: Aluminum Shell For Coils

## Slide 14: Aluminum Shell
Built by UT Knoxville Machine shop
Drum is ¼ inch rolled Aluminum
Two end plates are ¼ inch Aluminum sheet
Square insets on end plates are machined to 0.040 inches for neutron beam.
Designed to be filled with He-4 at one atmosphere to mitigate neutron scattering in the device.

## Slide 15: Details of Outer Coils
CAD drawings created using AutoDesk Inventor
Manufactured using 3D print Technology: Quickparts/ Proparts out of Atlanta
Coils manufactured using a laser sintering process in a vat of liquid resin (8 hours)
Precision manufacture to ~0.1 mm
Complete parts are ABS plastic

## Slide 16: Pictures of Outer Coils

## Slide 17: Summary
Design and Construction is essentially complete
Electrical tests are complete
Device scheduled for install this summer
Special Thanks to:
Chris Crawford, PhD: University of Kentucky, Lexington
Leading Expert on Cosine-Theta coils
Ricky Huff and Alvin Peak:
University of Tennessee machine shop