## Slide 1: n3He Experiment: Spin Flipper and Neutron Polarimetry
Christopher Hayes
November 13th, 2014

## Slide 2: Neutron Scattering on He-3
Goal is Statistical Observation of Parity Violation in the Hadronic Weak Interaction (HWI)
Observable is which represents a correlation between the spin of the incoming neutron and the momentum of the outgoing proton

## Slide 3: Theory of the Weak Hadronic Interaction
HWI described by the Meson Exchange Model.
Theory requires 6 coupling constants which must be measured experimentally.
Only three of 6 terms are significant for n3he.
For n3He Experiment:
+ small terms

## Slide 4: Neutron Beam at the SNS
SNS designed to provide high intensity 60 Hz pulses of neutrons
Source of neutrons is a 60 Hz
1 megawatt proton beam
colliding with a liquid Mercury
target
2 x1010 neutrons per second entering FNPB
Beam
Choppers
Neutrons
Neutrons
Neutrons
To n3He

## Slide 5: Schematic of the n3He Experiment
Neutron Guide
Super Mirror Polarizer
Beam Collimator
Beam Collimator
He-3
Ion Chamber
Uniform External Magnetic Field (~10 G)
DAQ
Computer
RFSR
(Spin Flipper)

## Slide 6: Ion Chamber
Frame stack holds alternating planes of high voltage and signal wires
17 High Voltage Wire Planes
16 Signal Wire Planes
144 Signal Wires Total

## Slide 7: Ion Chamber with Mount
Four Pre-Amplifier boxes connected to the Ion chamber

## Slide 8: Currents in Wire Planes
N

## Slide 9: Four Jaw Collimator
Doors covered with Li-6 and Cd which absorbs 99% of beam
Adjustable doors can transmit a beam of any height and width

## Slide 10: Requirements for a Spin Flipper
We want to build device that:
Must have a self-contained uniform B-field which will not interfere with the function of the target chamber, delicate DAQ electronics, or any other aspect of the experiment which can produce a false asymmetry.
Uses Spin Magnetic Resonance (SMR) to flip spins of all neutrons in the chopped beam (2.5 – 6.5A) with an efficiency approaching 100%.
Exists in a compact space and does not alter/interfere with the neutron beam.

## Slide 11: Design of a Cosine Theta Coil
Surface Current Density:
Fields determined using theory
of a magnetic scalar potential:
Wires on end caps routed along equi-potentials

## Slide 12: Fields of a Cosine Theta Coil
Magnetic analog of electrostatic problem using a charge density glued to the cylinder wall.

## Slide 13: Design of a Double Cosine-Theta Coil
Two Concentric Cosine theta coils
Currents flow in opposite directions
Approximation of infinite coil still valid

## Slide 14: Fields of a Double Cosine Theta Coil
--A way to produce a self-contained magnetic field that doesn’t interfere with anything else.

## Slide 15: Spin Magnetic Resonance
Drive the Spin Flipper at the Larmor frequency of neutrons in the 10 Gauss B-field
Spin Flipper
N
N
Perturbed field inside the spin flipper rotates the state ket

## Slide 16: Flipping Neutrons with a Wavelength Spectrum 2.5 – 6.5 A
To flip all neutrons in the beam, add a 1/t time dependence to envelope
B oscillates ~500 times within each envelope
Energy of neutrons in the beam is function of TOF with well defined arrival times

## Slide 17: Double Cosine Theta Coil as a Resonant Circuit
RFSR
R = 9.11 ohms
L = 2.01 mH
C = 17.70 nF
f = 26.655 +/- 0.005 kHz
Choose capacitor so that the circuit resonance at the Larmor Frequency

## Slide 18: Spin Flipper for the n3He Experiment

## Slide 19: Pictures of Inner Cylinder

## Slide 20: Pictures of Outer Coils

## Slide 21: Details of Outer Coils
CAD drawings created using AutoDesk Inventor
Manufactured using 3D print Technology: Quickparts/ Proparts out of Atlanta
Coils extruded using SLA laser curing of a liquid resin (8 hours)
Precision manufacture to ~0.1 mm
Completed parts were a plastic
replica of the CAD drawings

## Slide 22: Aluminum Shell/Housing
Shell Made by UT machine shop
Shell is ¼ inch Aluminum
Feed thru holes are used to fill interior with 4He.
Housing holds two capacitors in parallel:

## Slide 23: Field simulations for a Double Cosine-Theta Coil
BX
By

## Slide 24: Field Measurements on the Spin Flipper
Chart: Field Measurements at the End of the Spin Flipper
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Location 2 | 0.002 | 0.004 | 0.006 | 0.051 | 0.217 | 0.216 | 0.216 | 0.216 | 0.216 | 0.214 | 0.214 | 0.216 | 0.216 | 0.216 | 0.216
Chart: Field Measurements at the End of the Spin Flipper
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
 | 0.002 | 0.004 | 0.004 | 0.065 | 0.216 | 0.217 | 0.217 | 0.216 | 0.216 | 0.216 | 0.216 | 0.216 | 0.216 | 0.216 | 0.216
Blue Curve
Red Curve

## Slide 25: Neutron Polarimetry
Essential Part of the n3He experiment:
………. Polarization of Neutron Beam ~95%
…….. Spin Flipper Efficiency ~100%

## Slide 26: Polarimetry on a Beam of Neutrons
Ion Chamber
Spin Flipper
Analyzer
Beam
Monitor
Neutrons
Computer

## Slide 27: Properties of a 3He Cell
Hedy Lamarr
Filled with: 3He, N2, Rb
Individual 3He nuclei can be polarized thru Spin Exchange Optical Pumping
N
P
P
N
N
P
P
N

## Slide 28: Spin Exchange Optical Pumping
3HeCell
Laser
(795nm)
Oven
3He placed in a 10 Gauss external field and heated to 195 C to vaporize Rb Metal
Laser light interacts with vaporized Rb allowing it to transfer polarization to 3He nuclei thru hyperfine interaction
Cell polarizes overnight
¼ wave plate
Helmholtz coils

## Slide 29: Unpolarized Beam Thru Unpolarized Cell
3HeCell
Neutrons
Neutrons

## Slide 30: Transmissions thru a Polarized Cell
Analyzing Power of the 3He cell:

## Slide 31: Polarimetry with a Spin Flipper
Final element for doing neutron polarimetry is to introduce the Spin Flipper
Spin flipper flips individual SNS pulses at 60 Hz
Neutrons
Spin Flipper
Spin Flipper

## Slide 32: Measuring Beam Polarization with the Spin Flipper
SF
SF
SF

## Slide 33: Measuring Spin Flipper Efficiency
SF
SF
SF
SF

## Slide 34: Tuning Bo to the Spin Flipper
Perform separate measurements of SFR while varying the value of Bo near maximum
Find a least squares parabolic fit to acquired SFR data points.
Adjust Bo to optimal setting

## Slide 35: Accomplishments since May 2013
Completed all aspects of the design, construction, and testing of the Spin Flipper
Completed design and construction of the 4-Jaw collimator
Completed design of the V-Block/Sled alignment hardware
Completed design of two XY scanner mounts for location of Beam Centroid
Major contributor to the design/construction/implementation of the alignment laser beam
Major role in completing alignment of B-field in the cave
Presentations on the spin flipper for APS and ACNS

## Slide 36: Plan for n3He Polarimetry Measurements
Nov-Dec 2014: Polarimetry 1 (Preliminary test)
Beam Down: Dec 22nd 2014 – Feb 6th, 2015
Feb 6th, 2015: Polarimetry 2 (Pre-production)
Jun 20th, 2015: Polarimetry 3 (Intermediate)
Beam Down: June 22, 2015 – Aug 8th 2015
Aug 9th, 2015: Polarimetry 4 (Pre-production)
Dec 22nd, 2015: Polarimetry 5 (Final)

## Slide 37: n3He Collaboration