## Slide 1: XY Scanner Mount

## Slide 2: Back View
Screen Dimensions: 40 x 30 cm
15.75 x 13 inches
Screen: 1/8 inch aluminum
1/16 inch cadmium
1/4 inch Lithium
Beam Monitor with Pre-amp

## Slide 3: Front View
Opening for beam monitor:
1 cm x 1 cm
80 x 80 Kanya beam connects mount assembly to XY Tables

## Slide 4: Mount with Screen Removed
Easy removal of screen which can be used on both XY tables.
Easy removal of beam monitor and pre-amplifier also used on both xy tables.

## Slide 5: Front Plate
Three 3/16 holes for attaching front plate to screen
Seven 3/16 holes attach front plate to mount
Holes for laser alignment
Coordinates from center of aperture:
(-2.5, -3.45) and (-1.5, -3.45)

## Slide 6
XY Table (approximate size)
Scanner Mount Assembly
NPDGamma coils
Boxes show position of beam and 5 cm fringes around beam

## Slide 7
Inner box is 10 x 12 cm
Outer box is 20 x 22cm
At one centimeter increments we will have
440 beam monitor measurements
to determine centroid.
Motion inside coils is limited
Collision Protection ??
Some beam will escape screen
especially downstream

## Slide 8
Need to move about
8.5 inches in the horizontal direction
Vertical motion constrained by screen
(not shown here)