## Slide 1
Major issue:
How to define a run? It should be by #of T0s taken
Either by taking a certain number of samples for each T0 trigger (hasn’t been tried)
By taking data during a gate of some length, that starts for each T0 (tried)
However, I don’t think we’ve tried taking data for a fixed length  i.e. it’s always continuous until the process is killed.
11/26 Notes
Averaging
There appears to be a built in functionality to specify 2 clockrates:
Cockrate IN (a high one) and clockrate OUT (some lower one, that requires averaging of signals).
Some testing has already taken place  need more

## Slide 2
Thoughts on triggering
NOW (?)  “take_run frequncy”
Only pass it the frequency for data taking, daq runs, writing/overwriting files until stopped
Possibility 1 – Kabir/David tried it
Gates, data is taken in 16.4 ms increments, for 164 samples into 41 tbins  NIM gates aren’t good to 100us
Maybe: Can run with longer gates (16.55 ms) and only use 16.4 ms of data that we want. Not elegant, but would probably work
Possibility 2
Run continuously, but insert “event markers” into the data stream.
T0 signals would serve as event markers
Then, analyze as my data as we can before the next “event marker”
Possibility 3 – NPDGamma configuration (if can be implemented)
“take_data run_length samples”
Where run_length would define how long to take data for before gracefully stopping
Samples would specify how many samples to collect for each T0.
The system would need to be able to respond to T0 as triggers, not gates.