## Slide 1: Measuring the Electric Dipole Moment of the Neutron
Hena Kachroo

## Slide 2: Background
The Big Bang Theory
  Equal parts of matter and antimatter should have been created
  Now it is predominantly matter
  Explanation?

## Slide 3: Background
Neutron electric dipole moment (nEDM)
Violates Temporal and Charge Parity Symmetry
  Temporal symmetry: time reversal
  Parity: mirror image interactions
  Charge Parity: particle ↔︎ antiparticle
Neutron’s spin magnetic moment changes with reversal of time but EDM does not – violates Temporal symmetry
Notes: Symmetries: properties of a physical system that remain unchanged under the standard model of physics.

## Slide 4: Measuring the nEDM
Slow neutrons down, confine, and watch
Exposed to magnetic fields → measure precession frequency
  Nuclear reaction with He – 3
If EDM were present, spin axis would precess when exposed to field
Precession frequency shifts according to strength of field

## Slide 5: This Project
Neutrons = hypersensitive to magnetic fields
  Magnetic moment is large – precesses significantly in a weak field
  If not uniform – neutrons precess differently at different points
Design of uniform field is crucial
This project: designing a uniform magnetic field to help in testing for nEDM

## Slide 6: Design Elements
Double cosine theta coil
  2 cylindrical layers
  Prevents fringe field
Aluminum skeleton
Resin skins surround skeleton
Clips on skin

## Slide 7: Skin
Skin printed in sections of ¼ the skeleton
  Repeated for outer and inner sections
Skins have small pegs
  Pegs will fit into each other

## Slide 8: Skin
Adjustments made to skin:
  Pegs made smaller
  Dimensions changed
  Addition of lip to cover top and bottom of skeleton

## Slide 9: Clips
Clips line equipotential lines
Design of clips:
  Trenches
  Short clips
  Small enough to hold wire in precisely

## Slide 10: Clips Design
  Trench
  Clip
  Digout

## Slide 11: Summary
Designing a uniform magnetic field using a 3D printer
Coil used in measuring the nEDM
Detection of nEDM would help to explain the imbalance between matter and antimatter