## Slide 1: Electrify Everything! Joe Straley
Making everything run on electricity is a necessary step in the transition from fossil fuels. Starting that process immediately is also necessary, and helpful both to the process and the environment.

## Slide 2: Is the temperature increasing? (2010)

## Slide 3: The earth’s temperature is increasing

## Slide 4: Global Warming is Happening
By RCraig09 - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=88535596

## Slide 5: And we know why
C. D. Keeling, S. C. Piper, R. B. Bacastow, M. Wahlen, T. P. Whorf, M. Heimann, and H. A. Meijer

## Slide 6: We need to move away from fossil fuels
To prevent future warming
To prevent ocean acidification
For energy security
For better air quality
  Small particles
  Heavy metals
  Acid rain

## Slide 7: Where energy comes from now

## Slide 8: How to get from here to there:
Nuclear power
Wind power
Solar power
Hydropower
Minor resources
(geothermal, … , nuclear fusion)
How soon can these replace fossil fuels?

## Slide 9: How to get from here to there:
Nuclear power
Wind power
Solar power
Hydropower
Minor resources
(geothermal, … , nuclear fusion)
How soon can these replace fossil fuels?

## Slide 10: How to get from here to there: Nonfossil power is electrical power
Nuclear power
Wind power
Solar power
Hydropower
Minor resources
(geothermal, … , nuclear fusion)
How soon can these replace fossil fuels?

## Slide 11: Saul Griffiths

## Slide 13: Electrify everything now!
To be ready when the nonfossil resources come online
The lifetime of stoves, furnaces, water heaters, cars, ... range from 5 to 25 years. Electrify now to avoid this source of inertia

## Slide 14: Electrify everything now!
To be ready when the nonfossil resources come online
The lifetime of stoves, furnaces, water heaters, cars, ... range from 5 to 25 years. Electrify now to avoid this source of inertia
The Nonfossil Energy Future is an Electrical Future

## Slide 15: Electrify everything! Advantages
Central power plant conversion of fossil fuels to electrical energy is the most efficient method
  Combined-cycle gas 50-60%
  Coal-fired power 33%
  Gasoline automobile engine 20%
  Diesel engine 40%
  Electric car 85% (battery energy into motion)
Running an electric car on coal plant electricity is more efficient than a gasoline power car: 85% x 33% > 20%

## Slide 16: Electrify everything! Advantages
Conversion of as many power uses to electricity builds the grid and makes the energy economy “renewable ready.”
Provide demand for more electricity.

## Slide 17: Electrify
Furnaces and water heaters  heat pumps
Cooking with electricity
Transportation  electric car
Electrical devices often use the energy more efficiently.

## Slide 18: Home heating and water heating
A furnace for a 2,000 sq.ft. house would deliver 100,000 BTU/h = 30 KW.
A corresponding heat pump would need 10 KW if the temperature is 40 F = 5 C but significantly more on the days that it is 10 F = - 10 C.
Heat pump water heaters are more economical than gas (they take longer to reheat a whole tankful).

## Slide 21: Power the grid?
Load balancing happens a different way

## Slide 22: Solar power intermittency

## Slide 23: Power the grid?
 To even out supply and demand fluctuations
Advantages
  Provides “inertia” to the grid
  Lots of capacity
  Widely distributed, tracks population and electrical demand
Disadvantages
  The car has to be connected to the grid
  The charger has to be reversible
  The owner has to agree to this
  Despite the large capacity, probably can’t count on a lot of accessible stored energy

## Slide 24: Electrical devices are more energy efficient
Energy efficient of gasoline cars is quite low – 20%
Electrification of transportation could decrease energy input by a factor of 4 – and this is 27% of the energy budget
Heat pumps deliver 2-3 times as much energy as is put into them

## Slide 25: Where does the electrical power come from?
“US energy use” is 1020 J/year =
= 3.2 x 1012 Watts
= 3200 Gigawatt
≈ 3200 large power plants !!!
Right now, the total US electrical power output is only 470 GW??

## Slide 26: Where does the electrical power come from?
“US energy use” is 1020 J/year =
= 3.2 x 1012 Watts
= 3200 Gigawatt
≈ 3200 large power plants !!!
Right now, the total US electrical power output is only 470 GW.
But the comparison isn’t right.

## Slide 27: Where does the electrical power come from?
“US energy use” is 1020 J/year = 3.2 x 1012 Watts = 3200 Gigawatt
6% is from renewables (“heat equivalent”)
4% becomes road paving and plastic goods (doesn’t need replacement)
So we “only” need to replace 2900 GW.

## Slide 28: Where does the electrical power come from?
“US energy use” is 2900 Gigawatt that needs to be replaced
2900 GW is the energy value of the fuels – the thermal input to power plants. But a lot of it is electricity production (940 GW of thermal energy becomes 470 GW of electricity) or heat used at low temperature (heat pumps can provide that at a big discount) or in inefficient devices (automobiles!).
We only need 1400 Gigawatts of electricity to replace it.

## Slide 29: 1400 GW!
US nuclear power plants : 96 GW (843,000 GWh/year)
US wind power : 43 GW (380,000 GWh/year) in 2021.
US hydroelectric plants : 30 GW (260,000 GWh/year)
US solar power : 13 GW (115,000 GWh/year) in 2021
Total 182 GW nonfossil energy
Total electrical power 470 GW

## Slide 30: Wind Solar

## Slide 32: How we’ll get there
High gasoline prices are making electric cars more economical, charge points are appearing all over the place, and they are getting favorable press.
The newly passed Inflation Reduction Act has tax write-offs for heat pumps, solar panels, and electric cars.

## Slide 33: Conclusion
Electrifying everything will decrease energy need and CO2 production, even before the development of nonfossil energy resources
Electrifying everything will be a challenge, but it can be done